# Material Certification on MnDOT, Federal Aid, State Fund & Design Build Projects (3/25/13)

- Pre Construction:

- Review project Proposal, Special Provisions, Plan & governing Standard Specification book, for sampling, testing & monitoring of material on the project.

- Review your “Project Summary of Independent Assurance Testing” for project I.A. requirements. If you have not received the summary for your project contact the district I.A. inspector.

- Review Certification requirements for all Testers / Monitors / Inspectors for the project.

- Review project roles & responsibilities with project Testers / Monitors / Inspectors.

- Determine if testing equipment to be used on project is in good working order & meets calibration requirements for the current construction year.

- Insure the Plants being used are certified to produce Agency mix.

- If using QA Inspection services other than Metro Inspection (Consultant Services), review Roles and Responsibilities with them to insure proper and complete Specification coverage of the plants and/or Field Inspection. Determine frequency and to whom lab reports will be sent.

- If using the QA plant Inspection services of Metro Inspection, call Mn/DOT Metro Inspection office @ (651-234-7360) to make prior arrangements and get approval for mix designs.

- During Construction:

- Review all current project Testers / Monitors / Inspectors for certification requirements.

- Track daily plant Bituminous & Concrete production for specification conformity.

- Track daily field material placement for specification conformity.

- If using the QA plant Inspection services of Metro Inspection, call their office @ (651-234-7360) to set up plant inspection with estimated mix quantities needed DAILY.

- Contact District Metro Independent Assurance @ (651-234-7356) to set up project reviews.

- Metro District Materials /IAI website http://www.dot.state.mn.us/metro/materials/index.html

- Post Construction:

- Determine & report any material exceptions for the project, along with a proper resolution.

- Submit and review fax-letters for any Concrete and Bituminous plant exceptions.(Metro Inspection or Consultant done).

- Complete the Project QC/QA Final Physical Tester / Sampler Inventory sheet.

- Compile all of the above into a Material Certification Packet, and submit for District Materials review & signature.

MnDOT Electronic Forms, Manuals & Other Sources:

- MnDOT Lab Manual:

http://www.dot.state.mn.us/materials/labmanual.html

- Schedule of Materials Control:

http://www.dot.state.mn.us/materials/labmcs.html

- Material Certification Exception Summary:

http://www.dot.state.mn.us/materials/certificationdocs/CertificationexceptionsSummaryp1.doc

- Bituminous related items:

http://www.dot.state.mn.us/materials/bituminous.html

- Concrete related items:

http://www.dot.state.mn.us/materials/concrete.html

- Grading and Base items:

http://www.dot.state.mn.us/materials/gradingandbase.html

- Technical Certification:

http://www.dot.state.mn.us/const/tcp/index.html

- Approved Products and Certified Products and Sources for Acceptance on Mn/DOT and Federal-aid Projects and Design Build Projects:

http://www.dot.state.mn.us/products/index.html

- Currently Active Technical Memorandums:

http://techmemos.dot.state.mn.us/